## Slide 1: 3WSA Project Meteo web-sevice for Atmospheric dispersion of pollutants
Alain Kabamba
Enterprise Solutions Project Manager ERDAS
Contributor: Yannick Vandeloise & Arnaud Degroof – SPACEBEL
OGC TC MetOc WG
10th March 2010

## Slide 2: The 3WSA research Project
3WSA stands for Wallonia World Wide Space Applications
Partners: SPACEBEL (lead), ERDAS, WALPHOT, CETIC, AMOS, CSL (ULg), CREACTION, VITROCISET, AQUAPOLE (ULg)
Planning: November 2007 - December 2010
Founding: Belgian Walloon Region - Plan Marshall
Goal: the development of a generic software platform providing access to useful data and services in the context of environment, security and mobility management
Technology: ESA SSE, Web portal, Web Services, OGC standards

## Slide 3: 3WSA concept
Citizens
Interoperability - Standard Services
Multi-applications
Support Service
Mobile tracking & Messaging
3WSA Platform
Internet/Intranet
Network of terrestrial sensors
Remote Sensing Satellites
Geolocation (GALILEO)
communication satellites
Infrastructure and logistic support
Applications
Land Security
People Safety
Industrial Risks
Natural Hazards
Environment
Mobility
Experts
Decision makers
3WSA Demonstrator:
  SEVESO risk management system - Including an atmospheric dispersion model of pollutants

## Slide 4: 1976: Seveso disaster, Italy
In 1976, an important industrial accident happened at a chemical plant in Seveso, Italy, manufacturing pesticies and herbicides.
Notes: In 1976, an important industrial accident happened at a chemical plant in Seveso, Italy, manufacturing pesticies and herbicides. A dense vapour cloud containing tetrachlorodibenzo-paradioxin (TCDD) was released from a reactor. Commonly known as dioxin, this was a poisonous and carcinogenic by-product of an uncontrolled exothermic reaction.

## Slide 5: 1976: Seveso disaster, Italy
Large quantities of the substance, lethal to man even in microgram doses, were dispersed in the environment which resulted in an immediate contamination of some ten square miles of land and vegetation
Notes: More than 600 people had to be evacuated from their home
2000 were treated for dioxin poisoning

## Slide 6: The Seveso Directives
In Europe, the Seveso accident lead to the adoption of legislation aimed at the prevention and control of such accidents
In 1982, the first EU Directive 82/501/EEC - so-called Seveso Directive - was adopted.
On 9 December 1996, the Seveso Directive was replaced by Council Directive 96/82/EC, so-called Seveso-II Directive
Firstly, the Directive aims at the prevention of major-accident hazards involving dangerous substances
Secondly, as accidents do continue to occur, the Directive aims at the limitation of the consequences of such accidents not only for man (safety and health aspects) but also for the environment (environmental aspect)

## Slide 7: The disaster management workflow
Before
Disaster
After
Preparing
disaster
scenarios
Emmergency
actions
Monitoring
Other actions
Data Collection (Seveso sites, roads, buildings, POIs, dangerous products)
Precalculation of the disaster impact (plume, dispersion etc..)
This is what is done today 3WSA can add some value
3WSA can add some value here for decision makers
This is the most decive time
time
Meteo data in
real time

## Slide 8: So how the real time scenario will be implemented in the 3WSA demo?
We will use the OGC WPS (Web Processing Service) to calculate on the fly the Atmospheric dispersion of pollutants available on the SEVESO site with some meteo input – wind speed and direction (served through OGC SOS currently but could have been OGC WCS or OGC WFS), elevation data input through OGC WCS… The processing engine is called AUSTAL2000.
Notes: Plutôt dispersion…

## Slide 9: Austal2000
AUSTAL2000 is an atmospheric dispersion model for simulating the dispersion of air pollutants in the ambient atmosphere. It was developed by Ing. Büro Janicke in Dunum, Germany under contract to the Federal Ministry for Environment, Nature Conservation and Nuclear Safety.
AUSTAL2000 Inputs:
Main input parameters (pollutant, emission sources, emission strengths,…)
Meteorological times series or dispersion class statistics (wind speed & direction)
Roughness length
Digital elevation model
Several gaseous substances are available: sulphur dioxide, nitrogen monoxide, nitrogen dioxide, nitrogen oxides, benzene, tetrachloroethylene, hydrogen fluoride, ammonia, mercury, unspecified, unrated odourant and rated odourant
For particulate matter, different classes of the aerodynamic diameter (1 to 4 and unknown) can be distinguished

## Slide 10: 3WSA Implementation based on ESA SSE & ERDAS technology
Meteorological data
BPEL Workflow (Services chaining)
Process
Pre-treatment
Post-treatment
Digital elevation model
Expert inputs
Study of atmospheric dispersion of pollutant plume
Expert
needs:
WCS
OGC 03-065r6
version 1.0
WPS
OGC 05-007r7
version 1.0
SOS
OGC 06-009r4
version 0.1.2b
WMS
OGC 06-042
version 1.3

## Slide 11: 3WSA Case study : Engis (Belgium)
Several industries (SEVESO and others)

## Slide 12: Examples (wind speed = 13 - 16 m/s)
Wind direction (10° - 30°)
Wind direction (190° - 210°)
Wind direction (280° - 300°)
Wind direction (100° - 120°)

## Slide 13: Meteo data access
It is not possible to access the meteorological data in real time in a standard way
3WSA Solution
Meteo data (XSL format) acquisition (Royal Meteorological Institute of Belgium )
Create meteo database
Populated the database
Create and deploy the SOS web application
When the WPS retrieves the SOS data, it converts them into the AUSTAL2000 format
 Really complicated process!! Meteo Data should be accessed through an open standard interface

## Slide 14: Input meteo Data
Royal Meteorological Institute of Belgium in XLS format…
I would have expected more “standard” data like
  METAR - METeorological Airport Report of the International Civil Aviation Organization (ICAO)
  BUFR - Binary Universal Form for the Representation of meteorological data of the World Meteorological Organization (WMO)
  RAOB - RAdiosonde Observation data format of the Environmental Research Services (ERS)
  …

## Slide 15: 3WSA OGC SOS
Based on the OGC Observation & Measurements pattern
O&M model suits meteorological observations (like windspeed, direction) well especially our use case, but its properties need to be very specific to enable interoperability in the meteorology community
Meteo stations = sensors of our SOS, not really suitable for Atmospheric dispersion which requires more values in space.
For our use case SOS was OK for filtering data (phenomena, time, spatial)
Notes: Sensor Observation Service

## Slide 16: Result of a GetObservation

## Slide 17: Result of a GetObservation

## Slide 18: Input Meteo data (format akterm of the German DWD) needed by AUSTAL2000
* AKTERM-test
* Time period 01/06/2006 to 01/06/2006
* anonymisierte
+ Anemometerhoehen (0.1 m): 32 41 57 74 98 144 200 244 283
AK 06478 2006 01 06 00 00 1 1 290 3 1 3 1 -999 9
AK 06478 2006 01 06 01 00 1 1 280 3 1 3 1 -999 9
AK 06478 2006 01 06 02 00 1 1 280 3 1 3 1 -999 9
AK 06478 2006 01 06 03 00 1 1 280 3 1 3 1 -999 9
Germany's National Meteorological Service, the Deutscher Wetterdienst (DWD), is responsible for meeting meteorological requirements arising from all areas of economy and society in Germany.

## Slide 19: Wind map ALADIN model- Belgium
More precise results by applying the model called ALADIN (Aire Limitée Adaption Dynamique Développement International)
Notes: Such models provide the necessary input for the more specialized pollution models. Moreover, we believe that, besides the chemicalreaction model output, a simple index taking into account only meteorological conditions may be useful for briefing decision makers who do not have a good knowledge of the atmospheric sciences.

## Slide 20: Our questions…
Which OGC standard should be used by the meteorological Institutes or organizations to deliver data by the means of web service?
  OGC SOS (Sensor Observation Service)
  OGC WCS (Web Coverage Service)
  OGC WFS (Web Feature Service)
These OGC interfaces describes interfaces for accessing data but not the data model - What data model should be used to insure interoperability?
Which standard format should be used to exchange Meteo data? Gridded data (WCS)? GML Observation? Observations & Measurements?

## Slide 21: 3WSA Contacts
3WSA Contacts:
  Yannick Vandeloise SPACEBEL yannick.vandeloise@spacebel.be
  Alain Kabamba ERDAS alain.kabamba@erdas.com
ESA SSE portal URL: http://services.eoportal.org