Met Ocean Profile Handling Time synthesis

0 How to use this doc :

This is a working document.

White background : inputs to the work of writing the Met Ocean BP. Background infos

Yellow background : infos subject to discussion

Green : phrasing proposed as a draft for the Met Ocean BP.

1 References :

[1]OGC 06-042, Web Map Service (WMS) Implementation Standard, version 1.3.0. 2007

[2] OGC 07-063r1, OpenGIS Web MapServices – Application for EO Products, version 0.3.3 2009

[3] teleconfs minutes

[4] Existing implementations (See Annex 1)

2 Time References in Docs of reference

Into [1] OGC 06-042, Web Map Service (WMS) Implementation Standard, version 1.3.0. 2007 There are references at time handling into the following §

3 Normative references...................................................................6

6.7.6 Temporal CS  ....................................................         ...........18

6.7.7 Other coordinate systems  ..................................................19

7.3.2 GetMap Request overview ...................................................33

7.3.3.12 TIME                                  ..................................................37

7.3.3.14 Other sample dimensions.................................................37

Annex C (normative) Handling multi-dimensional data.......... .....51

Annex D (normative) Web Map Service profile of ISO 8601 ........57

Annex F (normative) UML model.....................................................72

Annex H (informative) XML examples.............................................80

3 Proposal of § for Met Ocean Profile

3 Normative references...................................................................

Inputs to discuss :

Inconsistencies into [1]

“For undated references, the latest edition of the referenced document (including any

amendments) applies.

ISO 8601:2004, Data elements and interchange formats — Information interchange — Representation of dates and times “

BUT

In Annex D references to ISO8601:2004 and ISO8601:2000

## Specific use case

A use case was submitted to give access to climatology statistics via a request with an incomplete time value into the GetMap (for example a time without the year element which doesn't seem to be compliant ISO 8601) example : average temperature over many years for a specific day of the month.

Proposal

ISO 8601:2004, will be the basic reference as stated into [1] . Nevertheless  if  ISO 8601:2000 is required to express an incomplete time (as for instance a time without the year to request a mean temperature for November) it will be usable as an extension for this specific need.

4 Terms and definitions ...................................................................

4.X sample dimension

dimension other than the four space-time dimensions [OGC 06-042]

6.7.6 Temporal CS  ...............................................................18

Page 11, the EO Profile states : “The use of the mandatory TIME dimension to retrieve maps from individual EO products is defined in subclause 7.3.1. Because the specification of a TIME value in a GetMap request is mandatory, the „default‟ attribute shall not be provided with the TIME dimension service metadata.”

How do we choose to stick to [1] or [2] ? Most of the present implementation stick to [1] and define a default as the last data available….

Proposal

When providing temporal information which is not continuous over the time axis and the client requests a TIME value which is not available,  the server may respond with a “nearest value” or a “best value”.

Note that when there is no exact match for the requested TIME value, the server response may include a „nearest value used‟ warning as per subclause C.4.3 of OGC 06-042.. This is compliant to OGC 07-063r1, OpenGIS Web MapServices – Application for EO Products, version 0.3.3 2009

6.7.7 Other coordinate systems  ...............................................................19

Inputs :

Considering the time, the description of Met Ocean data refers to several concepts :

1- The period covered by the forecast; the time domain of the forecast result. Called “phenomenonTime” in O&M2.0:

2- The time at which the last part of the numerical forecast run is made available = When the complete result are published Called  “resultTime” in O&M2.0

3- The Analysis Time that  describes the time instant for the initial conditions of a numerical weather simulation In O&M2.0 modelling , the Met Ocean modelling WG recommends to define a parameter called “analysisTime”:

The analysis Time is chosen from a time-instant toward the middle of the assimilation window where the model state is considered to be more realistic

4 The time period from which observations are selected to be assimilated into the analysis. In O&M2.0 modelling , the Met Ocean modelling WG recommends to define a parameter called “assimilationWindow”

Interval or period of accumulation ??? for precipitation accumulation, water waves…

Proposal

Meteorological and oceanographic data are multidimensional

The handling of service metadata for Meteorological and Oceanographic products defined here is in line with Annex C (Handling multi-dimensional data) of the WMS 1.3 standard (OGC 06-042). The overview for the WMS 1.3 handling of multi-dimensional data concludes:

“The server may declare a single name for the layer and enumerate available times and wavelength bands in its service metadata. A client then adds additional parameters to the GetMap request to request a specific time and band.”

Considering the time, the description of Met Ocean data can require several time dimensions and concepts.

For WMS implementations, two dimensions should be enough to describe the layers provided by a server :

TIME will be used for the validity date.

The numerical weather simulations are defined not only by their validity date but also by the time instant or period that was used as initial conditions for the simulations This dimension will be defined as follows :

Table X.X — Definition of ANALYSIS_TIME (or RUN_BASE_TIME) dimension

| Field | Mandatory / optional | Description |
| --- | --- | --- |
| name | M | ANALYSIS_TIME or RUN_BASE_TIME |
| units | M | ISO8601 |
| unitSymbol | O | none |
| default | O | Attribute indicating default value that will be used if GetMap request does not specify a value. If attribute is absent, then shall respond with a service exception if request does not include a value for that dimension. |
| multipleValues | O | Boolean attribute indicating whether multiple values of the dimension may be requested. 0 (or “false”) = single values only; 1 (or “true”) = multiple values permitted. Default = 0.. |
| nearestValue | O | Boolean attribute indicating whether nearest value of the dimension will be returned in response to a request for a nearby value. 0 (or “false”) = request value(s) must correspond exactly to declared extent value(s); 1 (or “true”) = request values may be approximate. Default = 0. |
| current | O | Boolean attribute valid only for temporal extents (i.e. if attribute name="time"). This attribute, if it either 1 or “true”, indicates (a) that temporal data are normally kept current and (b) that the request parameter TIME may include the keyword “current” instead of an ending value (see C.4.1). Default = 0. |
| extent | O | Text content indicating available value(s) for dimension. |

Examples :

Example of a service providing radar imagery products :

<Dimension name="time" units="ISO8601">2011-06-22T00:30:00Z/2011-06-27T13:50:00Z/PT5M</Dimension>

or

<Dimension name="time" units="ISO8601">2011-06-22T00:30:00Z,2011-06-22T00:45:00Z,2011-06-22T00:50:00Z,2011-06-22T01:15:00Z,2011-06-22T01:30:00Z,2011-06-22T01:45:00Z,2011-06-22T01:55:00Z,2011-06-22T02:00:00Z,2011-06-22T02:15:00Z,2011-06-22T02:30:00Z,2011-06-22T02:40:00Z,2011-06-22T02:45:00Z,2011-06-22T03:00:00Z</Dimension>

Example of a service providing satellite imagery products :

<Dimension name="time" units="ISO8601" default="2011-06-25T00:00:00Z" multipleValues="1" nearestValue="0">2010-01-01T00:00:00Z/2011-06-25T00:00:00Z/P1D</ Dimension >

Example1 of a service providing numerical model output :

<Dimension name="time" units="ISO8601" default="2011-06-22T06:00:00Z" multipleValues="0" nearestValue="0">2011-06-17T06:00:00Z,2011-06-17T09:00:00Z/2011-06-28T00:00:00Z/PT3H,2011-06-28T06:00:00Z/2011-07-02T00:00:00Z/PT6H</ Dimension >

or

<Dimension name="time" units="ISO8601" default="2011-06-22T06:00:00Z" multipleValues="0" nearestValue="0">2011-06-17T06:00:00Z,2011-06-17T09:00:00Z/2011-06-28T00:00:00Z/PT3H,2011-06-28T06:00:00Z/2011-07-02T00:00:00Z/PT6H</ Dimension >

<Dimension name="analysistime" units="ISO8601" default="2011-06-22T06:00:00Z" multipleValues="0" nearestValue="0">2011-06-13T06:00:00Z/2011-06-22T06:00:00Z/PT6H, </ Dimension >

7.3.2 GetMap Request overview

Proposal

Table 8 — The Parameters of a GetMap request

| Request parameter | Mandatory / optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=1.3.0 | M | Request version. | No change |
| REQUEST=GetMap | M | Request name. | No change |
| LAYERS=layer_list | M | Comma-separated list of one or more map layers. | No change |
| STYLES=style_list | M | Comma-separated list of one rendering style per requested layer. | No change |
| CRS=namespace:identifier | M | Coordinate reference system. | No change |
| BBOX=minx,miny,maxx,maxy | M | Bounding box corners (lower left, upper right) in CRS units. | No change |
| WIDTH=output_width | M | Width in pixels of map picture. | No change |
| HEIGHT=output_height | M | Height in pixels of map picture. | No change |
| FORMAT=output_format | M | Output format of map. | No change |
| TRANSPARENT=TRUE¦FALSE | O | Background transparency of map (default=FALSE). | ?? |
| BGCOLOR=color_value | O | Hexadecimal red-green-blue colour value for the background color (default=0xFFFFFF). | ?? |
| EXCEPTIONS=exception_format | O | The format in which exceptions are to be reported by the WMS (default=XML). | No change |
| TIME=time | O | Time value of layer desired. | Recommanded |
| ELEVATION=elevation | O | Elevation of layer desired. | ?? |
| ANALYSIS_TIME | O | time instant or period that was used as initial conditions for the simulations | Default value to define to last run or best run |
| Other sample dimension(s) | O | Value of other dimensions as appropriate. | ?? Add more detail e.g. 2nd time probability threshold |

7.3.3.12 TIME                                  ..................................................37

The request to servers providing Met Ocean information should use the TIME parameter.

Nevertheless, 6.7.6 recommends a server should declare a default value in service metadata, and a server shall respond with the default value if one has been declared and the client request does not include a value. When providing temporal information which is not continuous over the time axis and the client requests a TIME value which is not available,  the server shall respond with a “nearest value” or a “best value”. .

This recommendation will improve interoperability but the client should define a TIME value to be able to  control the validity time of the data it requests.

7.3.3.14 Other sample dimensions.................................................37

The use of sample dimension values is specified in 6.7.7 of [1] completed by 6.7.7  of this document and in Annex C of [1] .

Annex C (normative) Handling multi-dimensional data...............

TBC

Annex D (normative) Web Map Service profile of ISO 8601 ........

No Change

Annex F (normative) UML model.....................................................

TBC

Annex H (informative) XML examples.............................................

TBC

ANNEX 1 : Examples of existing implementations for time handling

<Dimension name="RUN" units="ISO8601" />

<Dimension name="FORECAST" units="ISO8601" />

<Dimension name="RUN" units="ISO8601" default="2011-06-24T00:00:00">2011-06-23T00:00:00,2011-06-23T06:00:00,2011-06-23T12:00:00,2011-06-23T18:00:00,2011-06-24T00:00:00</Dimension>

<Dimension name="FORECAST" units="ISO8601" default="PT0S">PT0S,PT3H,PT6H,PT9H,PT12H,PT15H,PT30H,PT33H,PT36H,PT39H,PT42H,PT45H,PT48H,PT54H,PT60H,PT66H,PT72H,PT78H,PT84H,PT90H,PT96H,PT102H,PT108H,PT114H,P5DT,P5DT12H,P6DT,P6DT12H,P7DT,P7DT12H</Dimension>

--------------------------------------------------------------------------------------------------------

<Dimension name="time" units="ISO8601" />

<Extent name="time" default="2011-06-22T00:00:00Z" multipleValues="0" nearestValue="0">2011-06-17T00:00:00Z,2011-06-17T03:00:00Z/2011-06-28T00:00:00Z/PT3H,2011-06-28T06:00:00Z/2011-07-07T00:00:00Z/PT6H</Extent>

<Dimension name="interval" units="hour" />

<Extent name="interval" default="6" multipleValues="0" nearestValue="0">3,6,9,12,24,48</Extent>

--------------------------------------------------------------------------------------------------------

<Dimension name="time" units="ISO8601" multipleValues="true" current="false" default="2006-01">2006-01/2099-12/P1M</Dimension>

--------------------------------------------------------------------------------------------------------

<Dimension name="time" units="ISO8601" />

<Extent name="time" default="2011-06-26T10:35:00Z" multipleValues="1" nearestValue="0">2009-03-27T13:50:00Z/2011-06-26T10:35:00Z/PT5M</Extent>

<Dimension name="time" units="ISO8601" multipleValues="true" current="true" default="2011-06-27T06:00:00.000Z">2011-05-10T00:00:00.000Z,2011-05-10T03:00:00.000Z,2011-05-10T06:00:00.000Z,2011-05-10T09:00:00.000Z,2011-05-10T12:00:00.000Z,2011-05-10T15:00:00.000Z,2011-05-10T18:00:00.000Z,2011-05-10T21:00:00.000Z,2011-05-11T00:00:00.000Z,2011-05-11T03:00:00.000Z,2011-05-11T06:00:00.000Z,2011-05-11T09:00:00.000Z,2011-05-11T12:00:00.000Z,2011-05-11T15:00:00.000Z,2011-05-11T18:00:00.000Z,2011-05-11T21:00:00.000Z,2011-05-12T00:00:00.000Z,2011-05-12T03:00:00.000Z,2011-05-12T06:00:00.000Z,2011-05-12T09:00:00.000Z,2011-05-12T12:00:00.000Z,2011-05-12T15:00:00.000Z,2011-05-12T18:00:00.000Z,2011-05-12T21:00:00.000Z,2011-05-13T00:00:00.000Z,2011-05-13T03:00:00.000Z,2011-05-13T06:00:00.000Z,2011-05-13T09:00:00.000Z,2011-05-13T12:00:00.000Z,2011-05-13T15:00:00.000Z,2011-05-13T18:00:00.000Z,2011-05-13T21:00:00.000Z,2011-05-14T00:00:00.000Z,2011-05-14T03:00:00.000Z,2011-05-14T06:00:00.000Z,2011-05-14T09:00:00.000Z,2011-05-14T12:00:00.000Z,2011-05-14T15:00:00.000Z,2011-05-14T18:00:00.000Z,2011-05-14T21:00:00.000Z,2011-05-15T00:00:00.000Z,2011-05-15T03:00:00.000Z,2011-05-15T06:00:00.000Z,2011-05-15T09:00:00.000Z,2011-05-15T12:00:00.000Z,2011-05-15T15:00:00.000Z,2011-05-15T18:00:00.000Z,2011-05-15T21:00:00.000Z,2011-05-16T00:00:00.000Z,2011-05-16T03:00:00.000Z,2011-05-16T06:00:00.000Z,2011-05-16T09:00:00.000Z,2011-05-16T12:00:00.000Z,2011-05-16T15:00:00.000Z,2011-05-16T18:00:00.000Z,2011-05-16T21:00:00.000Z,2011-05-17T00:00:00.000Z,2011-05-17T03:00:00.000Z,2011-05-17T06:00:00.000Z,2011-05-17T09:00:00.000Z,2011-05-17T12:00:00.000Z,2011-05-17T15:00:00.000Z,2011-05-17T18:00:00.000Z,2011-05-17T21:00:00.000Z,2011-05-18T00:00:00.000Z,2011-05-18T03:00:00.000Z,2011-05-18T06:00:00.000Z,2011-05-18T09:00:00.000Z,2011-05-18T12:00:00.000Z,2011-05-18T15:00:00.000Z,2011-05-18T18:00:00.000Z,2011-05-18T21:00:00.000Z,2011-05-19T00:00:00.000Z,2011-05-19T03:00:00.000Z,2011-05-19T06:00:00.000Z,2011-05-19T09:00:00.000Z,2011-05-19T12:00:00.000Z,2011-05-19T15:00:00.000Z,2011-05-19T18:00:00.000Z,2011-05-19T21:00:00.000Z,2011-05-20T00:00:00.000Z,2011-05-20T03:00:00.000Z,2011-05-20T06:00:00.000Z,2011-05-20T09:00:00.000Z,2011-05-20T12:00:00.000Z,2011-05-20T15:00:00.000Z,2011-05-20T18:00:00.000Z,2011-05-20T21:00:00.000Z,2011-05-21T00:00:00.000Z,2011-05-21T03:00:00.000Z,2011-05-21T06:00:00.000Z,2011-05-21T09:00:00.000Z,2011-05-21T12:00:00.000Z,2011-05-21T15:00:00.000Z,2011-05-21T18:00:00.000Z,2011-05-21T21:00:00.000Z,2011-05-22T00:00:00.000Z,2011-05-22T03:00:00.000Z,2011-05-22T06:00:00.000Z,2011-05-22T09:00:00.000Z,2011-05-22T12:00:00.000Z,2011-05-22T15:00:00.000Z,2011-05-22T18:00:00.000Z,2011-05-22T21:00:00.000Z,2011-05-23T00:00:00.000Z,2011-05-23T03:00:00.000Z,2011-05-23T06:00:00.000Z,2011-05-23T09:00:00.000Z,2011-05-23T12:00:00.000Z,2011-05-23T15:00:00.000Z,2011-05-23T18:00:00.000Z,2011-05-23T21:00:00.000Z,2011-05-24T00:00:00.000Z,2011-05-24T03:00:00.000Z,2011-05-24T06:00:00.000Z,2011-05-24T09:00:00.000Z,2011-05-24T12:00:00.000Z,2011-05-24T15:00:00.000Z,2011-05-24T18:00:00.000Z,2011-05-24T21:00:00.000Z,2011-05-25T00:00:00.000Z,2011-05-25T03:00:00.000Z,2011-05-25T06:00:00.000Z,2011-05-25T09:00:00.000Z,2011-05-25T12:00:00.000Z,2011-05-25T15:00:00.000Z,2011-05-25T18:00:00.000Z,2011-05-25T21:00:00.000Z,2011-05-26T00:00:00.000Z,2011-05-26T03:00:00.000Z,2011-05-26T06:00:00.000Z,2011-05-26T09:00:00.000Z,2011-05-26T12:00:00.000Z,2011-05-26T15:00:00.000Z,2011-05-26T18:00:00.000Z,2011-05-26T21:00:00.000Z,2011-05-27T00:00:00.000Z,2011-05-27T03:00:00.000Z,2011-05-27T06:00:00.000Z,2011-05-27T09:00:00.000Z,2011-05-27T12:00:00.000Z,2011-05-27T15:00:00.000Z,2011-05-27T18:00:00.000Z,2011-05-27T21:00:00.000Z,2011-05-28T00:00:00.000Z,2011-05-28T03:00:00.000Z,2011-05-28T06:00:00.000Z,2011-05-28T09:00:00.000Z,2011-05-28T12:00:00.000Z,2011-05-28T15:00:00.000Z,2011-05-28T18:00:00.000Z,2011-05-28T21:00:00.000Z,2011-05-29T00:00:00.000Z,2011-05-29T03:00:00.000Z,2011-05-29T06:00:00.000Z,2011-05-29T09:00:00.000Z,2011-05-29T12:00:00.000Z,2011-05-29T15:00:00.000Z,2011-05-29T18:00:00.000Z,2011-05-29T21:00:00.000Z,2011-05-30T00:00:00.000Z,2011-05-30T03:00:00.000Z,2011-05-30T06:00:00.000Z,2011-05-30T09:00:00.000Z,2011-05-30T12:00:00.000Z,2011-05-30T15:00:00.000Z,2011-05-30T18:00:00.000Z,2011-05-30T21:00:00.000Z,2011-05-31T00:00:00.000Z,2011-05-31T03:00:00.000Z,2011-05-31T06:00:00.000Z,2011-05-31T09:00:00.000Z,2011-05-31T12:00:00.000Z,2011-05-31T15:00:00.000Z,2011-05-31T18:00:00.000Z,2011-05-31T21:00:00.000Z,2011-06-01T00:00:00.000Z,2011-06-01T03:00:00.000Z,2011-06-01T06:00:00.000Z,2011-06-01T09:00:00.000Z,2011-06-01T12:00:00.000Z,2011-06-01T15:00:00.000Z,2011-06-01T18:00:00.000Z,2011-06-01T21:00:00.000Z,2011-06-02T00:00:00.000Z,2011-06-02T03:00:00.000Z,2011-06-02T06:00:00.000Z,2011-06-02T09:00:00.000Z,2011-06-02T12:00:00.000Z,2011-06-02T15:00:00.000Z,2011-06-02T18:00:00.000Z,2011-06-02T21:00:00.000Z,2011-06-03T00:00:00.000Z,2011-06-03T03:00:00.000Z,2011-06-03T06:00:00.000Z,2011-06-03T09:00:00.000Z,2011-06-03T12:00:00.000Z,2011-06-03T15:00:00.000Z,2011-06-03T18:00:00.000Z,2011-06-03T21:00:00.000Z,2011-06-04T00:00:00.000Z,2011-06-04T03:00:00.000Z,2011-06-04T06:00:00.000Z,2011-06-04T09:00:00.000Z,2011-06-04T12:00:00.000Z,2011-06-04T15:00:00.000Z,2011-06-04T18:00:00.000Z,2011-06-04T21:00:00.000Z,2011-06-05T00:00:00.000Z,2011-06-05T03:00:00.000Z,2011-06-05T06:00:00.000Z,2011-06-05T09:00:00.000Z,2011-06-05T12:00:00.000Z,2011-06-05T15:00:00.000Z,2011-06-05T18:00:00.000Z,2011-06-05T21:00:00.000Z,2011-06-06T00:00:00.000Z,2011-06-06T03:00:00.000Z,2011-06-06T06:00:00.000Z,2011-06-06T09:00:00.000Z,2011-06-06T12:00:00.000Z,2011-06-06T15:00:00.000Z,2011-06-06T18:00:00.000Z,2011-06-06T21:00:00.000Z,2011-06-07T00:00:00.000Z,2011-06-07T03:00:00.000Z,2011-06-07T06:00:00.000Z,2011-06-07T09:00:00.000Z,2011-06-07T12:00:00.000Z,2011-06-07T15:00:00.000Z,2011-06-07T18:00:00.000Z,2011-06-07T21:00:00.000Z,2011-06-08T00:00:00.000Z,2011-06-08T03:00:00.000Z,2011-06-08T06:00:00.000Z,2011-06-08T09:00:00.000Z,2011-06-08T12:00:00.000Z,2011-06-08T15:00:00.000Z,2011-06-08T18:00:00.000Z,2011-06-08T21:00:00.000Z,2011-06-09T00:00:00.000Z,2011-06-09T03:00:00.000Z,2011-06-09T06:00:00.000Z,2011-06-09T09:00:00.000Z,2011-06-09T12:00:00.000Z,2011-06-09T15:00:00.000Z,2011-06-09T18:00:00.000Z,2011-06-09T21:00:00.000Z,2011-06-10T00:00:00.000Z,2011-06-10T03:00:00.000Z,2011-06-10T06:00:00.000Z,2011-06-10T09:00:00.000Z,2011-06-10T12:00:00.000Z,2011-06-10T15:00:00.000Z,2011-06-10T18:00:00.000Z,2011-06-10T21:00:00.000Z,2011-06-11T00:00:00.000Z,2011-06-11T03:00:00.000Z,2011-06-11T06:00:00.000Z,2011-06-11T09:00:00.000Z,2011-06-11T12:00:00.000Z,2011-06-11T15:00:00.000Z,2011-06-11T18:00:00.000Z,2011-06-11T21:00:00.000Z,2011-06-12T00:00:00.000Z,2011-06-12T03:00:00.000Z,2011-06-12T06:00:00.000Z,2011-06-12T09:00:00.000Z,2011-06-12T12:00:00.000Z,2011-06-12T15:00:00.000Z,2011-06-12T18:00:00.000Z,2011-06-12T21:00:00.000Z,2011-06-13T00:00:00.000Z,2011-06-13T03:00:00.000Z,2011-06-13T06:00:00.000Z,2011-06-13T09:00:00.000Z,2011-06-13T12:00:00.000Z,2011-06-13T15:00:00.000Z,2011-06-13T18:00:00.000Z,2011-06-13T21:00:00.000Z,2011-06-14T00:00:00.000Z,2011-06-14T03:00:00.000Z,2011-06-14T06:00:00.000Z,2011-06-14T09:00:00.000Z,2011-06-14T12:00:00.000Z,2011-06-14T15:00:00.000Z,2011-06-14T18:00:00.000Z,2011-06-14T21:00:00.000Z,2011-06-15T00:00:00.000Z,2011-06-15T03:00:00.000Z,2011-06-15T06:00:00.000Z,2011-06-15T09:00:00.000Z,2011-06-15T12:00:00.000Z,2011-06-15T15:00:00.000Z,2011-06-15T18:00:00.000Z,2011-06-15T21:00:00.000Z,2011-06-16T00:00:00.000Z,2011-06-16T03:00:00.000Z,2011-06-16T06:00:00.000Z,2011-06-16T09:00:00.000Z,2011-06-16T12:00:00.000Z,2011-06-16T15:00:00.000Z,2011-06-16T18:00:00.000Z,2011-06-16T21:00:00.000Z,2011-06-17T00:00:00.000Z,2011-06-17T03:00:00.000Z,2011-06-17T06:00:00.000Z,2011-06-17T09:00:00.000Z,2011-06-17T12:00:00.000Z,2011-06-17T15:00:00.000Z,2011-06-17T18:00:00.000Z,2011-06-17T21:00:00.000Z,2011-06-18T00:00:00.000Z,2011-06-18T03:00:00.000Z,2011-06-18T06:00:00.000Z,2011-06-18T09:00:00.000Z,2011-06-18T12:00:00.000Z,2011-06-18T15:00:00.000Z,2011-06-18T18:00:00.000Z,2011-06-18T21:00:00.000Z,2011-06-19T00:00:00.000Z,2011-06-19T03:00:00.000Z,2011-06-19T06:00:00.000Z,2011-06-19T09:00:00.000Z,2011-06-19T12:00:00.000Z,2011-06-19T15:00:00.000Z,2011-06-19T18:00:00.000Z,2011-06-19T21:00:00.000Z,2011-06-20T00:00:00.000Z,2011-06-20T03:00:00.000Z,2011-06-20T06:00:00.000Z,2011-06-20T09:00:00.000Z,2011-06-20T12:00:00.000Z,2011-06-20T15:00:00.000Z,2011-06-20T18:00:00.000Z,2011-06-20T21:00:00.000Z,2011-06-21T00:00:00.000Z,2011-06-21T03:00:00.000Z,2011-06-21T06:00:00.000Z,2011-06-21T09:00:00.000Z,2011-06-21T12:00:00.000Z,2011-06-21T15:00:00.000Z,2011-06-21T18:00:00.000Z,2011-06-21T21:00:00.000Z,2011-06-22T00:00:00.000Z,2011-06-22T03:00:00.000Z,2011-06-22T06:00:00.000Z,2011-06-22T09:00:00.000Z,2011-06-22T12:00:00.000Z,2011-06-22T15:00:00.000Z,2011-06-22T18:00:00.000Z,2011-06-22T21:00:00.000Z,2011-06-23T00:00:00.000Z,2011-06-23T03:00:00.000Z,2011-06-23T06:00:00.000Z,2011-06-23T09:00:00.000Z,2011-06-23T12:00:00.000Z,2011-06-23T15:00:00.000Z,2011-06-23T18:00:00.000Z,2011-06-23T21:00:00.000Z,2011-06-24T00:00:00.000Z,2011-06-24T03:00:00.000Z,2011-06-24T06:00:00.000Z,2011-06-24T09:00:00.000Z,2011-06-24T12:00:00.000Z,2011-06-24T15:00:00.000Z,2011-06-24T18:00:00.000Z,2011-06-24T21:00:00.000Z,2011-06-25T00:00:00.000Z,2011-06-25T03:00:00.000Z,2011-06-25T06:00:00.000Z,2011-06-25T09:00:00.000Z,2011-06-25T12:00:00.000Z,2011-06-25T15:00:00.000Z,2011-06-25T18:00:00.000Z,2011-06-25T21:00:00.000Z,2011-06-26T00:00:00.000Z,2011-06-26T03:00:00.000Z,2011-06-26T06:00:00.000Z,2011-06-26T09:00:00.000Z,2011-06-26T12:00:00.000Z,2011-06-26T15:00:00.000Z,2011-06-26T18:00:00.000Z,2011-06-26T21:00:00.000Z,2011-06-27T00:00:00.000Z,2011-06-27T03:00:00.000Z,2011-06-27T06:00:00.000Z,2011-06-27T09:00:00.000Z,2011-06-27T12:00:00.000Z,2011-06-27T15:00:00.000Z,2011-06-27T18:00:00.000Z,2011-06-27T21:00:00.000Z,2011-06-28T00:00:00.000Z,2011-06-28T03:00:00.000Z,2011-06-28T06:00:00.000Z,2011-06-28T09:00:00.000Z,2011-06-28T12:00:00.000Z,2011-06-28T15:00:00.000Z,2011-06-28T18:00:00.000Z,2011-06-28T21:00:00.000Z,2011-06-29T00:00:00.000Z,2011-06-29T03:00:00.000Z,2011-06-29T06:00:00.000Z,2011-06-29T09:00:00.000Z,2011-06-29T12:00:00.000Z,2011-06-29T15:00:00.000Z,2011-06-29T18:00:00.000Z,2011-06-29T21:00:00.000Z,2011-06-30T00:00:00.000Z,2011-06-30T03:00:00.000Z,2011-06-30T06:00:00.000Z,2011-06-30T09:00:00.000Z,2011-06-30T12:00:00.000Z,2011-06-30T15:00:00.000Z,2011-06-30T18:00:00.000Z,2011-06-30T21:00:00.000Z,2011-07-01T00:00:00.000Z,2011-07-01T03:00:00.000Z,2011-07-01T06:00:00.000Z,2011-07-01T09:00:00.000Z,2011-07-01T12:00:00.000Z,2011-07-01T15:00:00.000Z,2011-07-01T18:00:00.000Z,2011-07-01T21:00:00.000Z,2011-07-02T00:00:00.000Z,2011-07-02T03:00:00.000Z,2011-07-02T06:00:00.000Z,2011-07-02T09:00:00.000Z,2011-07-02T12:00:00.000Z,2011-07-02T15:00:00.000Z,2011-07-02T18:00:00.000Z,2011-07-02T21:00:00.000Z,2011-07-03T00:00:00.000Z,2011-07-03T03:00:00.000Z,2011-07-03T06:00:00.000Z,2011-07-03T09:00:00.000Z,2011-07-03T12:00:00.000Z,2011-07-03T15:00:00.000Z,2011-07-03T18:00:00.000Z,2011-07-03T21:00:00.000Z,2011-07-04T00:00:00.000Z,2011-07-04T03:00:00.000Z,2011-07-04T06:00:00.000Z,2011-07-04T09:00:00.000Z,2011-07-04T12:00:00.000Z,2011-07-04T15:00:00.000Z,2011-07-04T18:00:00.000Z,2011-07-04T21:00:00.000Z,2011-07-05T00:00:00.000Z</Dimension>

<Dimension name="time" units="ISO8601">2011-06-22T00:30:00Z,2011-06-22T00:45:00Z,2011-06-22T00:50:00Z,2011-06-22T01:15:00Z,2011-06-22T01:30:00Z,2011-06-22T01:45:00Z,2011-06-22T01:55:00Z,2011-06-22T02:00:00Z,2011-06-22T02:15:00Z,2011-06-22T02:30:00Z,2011-06-22T02:40:00Z,2011-06-22T02:45:00Z,2011-06-22T03:00:00Z</Dimension>